## Slide 1
Smart Visual Alarm System
Ernyei Zoltán | MAT. 265056
ESP32-S3-EYE local detection
Telegram alarm from MQTT metadata
Frames stay on the board. Only alarm metadata leaves the device.
ESP-DL
embedded inference
PedestrianDetect on ESP32-S3
MQTT
event transport
JSON topic payload
Telegram
notification
Bot API sendMessage
Smart Visual Alarm System | 01
Notes: Open by saying that this project is a complete visual alarm prototype built around the ESP32-S3-EYE board. The board runs the people detector locally, so the camera image is not sent to a cloud model. The alarm is converted into a small MQTT JSON event, and a Python script forwards that event to the Telegram bot. Point to the two images: the board display proves the local detection, and the Telegram screenshot proves the notification path.

## Slide 2
Requirements drive the runtime design
Embedded vision
ESP32-S3-EYE camera frame acquisition
LCD preview with detection overlay
camera frames stay on the device
On-device AI
ESP-WHO / ESP-DL pedestrian detector
confidence threshold for valid candidates
bounding-box output for visual feedback
Event control
confirmation frames before an alarm
cooldown to avoid repeated alerts
compact JSON metadata payload
Notification bridge
MQTT topic transport
Python validation and formatting
Telegram Bot API user notification
Core flow: detect locally -> confirm event -> publish MQTT -> notify Telegram
Smart Visual Alarm System | 02
Notes: Explain this slide as the requirement baseline for the system. The project is not just a camera demo: it needs embedded vision, a clear alarm policy, a network event format, and a user notification bridge. Each block maps to a real component in the implementation, which keeps the architecture easy to explain and easy to verify.

## Slide 3
Six-stage alarm path
01
Camera
ESP32-S3-EYE onboard camera captures RGB565 frames.
02
Inference
ESP-WHO task runs PedestrianDetect locally.
03
Policy
Threshold + repeated frames confirm an alarm.
04
MQTT
Firmware publishes compact JSON event metadata.
05
Backend
Python subscriber validates and formats the alert.
06
Telegram
Bot message reaches the configured chat.
ESP-IDF v5.5.2
ESP-WHO / ESP-DL
Mosquitto broker
paho-mqtt + requests
Telegram Bot API
Boundary rule: raw camera frames stay on the ESP32-S3-EYE. The network event contains label, confidence, count, time, and box coordinates.
Smart Visual Alarm System | 03
Notes: Walk left to right. The ESP32-S3-EYE captures frames, the detector runs on-device, the policy waits for repeated positive frames, and only then the firmware publishes MQTT JSON. The backend is a separate Python process on the laptop. It subscribes to the topic and sends a Telegram message. The slide also lists the real technologies used: ESP-IDF, ESP-WHO/ESP-DL, Mosquitto, paho-mqtt, requests, and Telegram Bot API.

## Slide 4
ESP32-S3-EYE runtime loop
1
Boot
Initialize LEDs, LCD preview, Wi-Fi/MQTT client
2
Frame capture
ESP-WHO camera pipeline acquires RGB565 frames
3
Detect
PedestrianDetect returns boxes and confidence scores
4
Preview
LCD overlays the strongest person candidate
5
Confirm
Threshold + consecutive frames + cooldown
6
Publish
MQTT JSON alarm event, or serial log fallback
Tunable Kconfig controls
score threshold
confirmation frame count
alert cooldown seconds
device ID, broker URI, topic
Defensive networking
If Wi-Fi or MQTT is not configured, detections still run and alarm JSON is logged over serial.
Core files: app_main.cpp, alarm_mqtt.cpp, lcd_preview.cpp, frame_cap_pipeline.cpp
Smart Visual Alarm System | 04
Notes: This slide explains what happens inside the firmware. The firmware starts the board hardware, begins capture, runs the detector, draws a visual bounding box on the LCD, and then applies the alarm policy. The policy is important because it prevents a single noisy frame from creating a Telegram message. Also mention that the firmware can keep running without network setup and log JSON over serial, which helps debugging.

## Slide 5
The pedestrian model runs fully on the ESP32-S3
PICO_S8_V1
model variant
Espressif pedestrian_detect v0.3.0
435,328 B
parameter storage
compiled .espdl blob in flash
224x224x3
input tensor
RGB image resized before inference
118.3 ms
reported model step
Espressif ESP32-S3 timing
1
Frame
RGB565 camera frame from ESP32-S3-EYE
2
Preprocess
resize and format for 224x224x3 input
3
Infer
PedestrianDetect calls ESP-DL model locally
4
Result
person box and confidence score returned
Model artifact: pedestrian_detect_pico_s8_v1.espdl | Runtime: ESP-WHO + ESP-DL on ESP32-S3
Smart Visual Alarm System | 05
Notes: Explain that the AI model is not running on a laptop or cloud API. The firmware embeds Espressif's PICO_S8_V1 pedestrian detector as an ESP-DL model artifact. The compiled model blob is 435,328 bytes in flash, the input is 224 by 224 by 3, and the reported model inference step on ESP32-S3 is around 118.3 ms. The detector produces a bounding box and confidence score, and the alarm policy decides whether that result becomes an alert.

## Slide 6
Confirmed detections become MQTT events
1
candidate seen
2
threshold passed
N
repeated frames
!
publish event
30s
cooldown
6+
required fields
event, device, time, label, confidence, frames
0..1
alarm quality
confidence score kept in payload
box
debug evidence
x_min, y_min, x_max, y_max
{
"device_id": "esp32s3-eye-01",
"label": "person",
"confidence": 0.824,
"confirmation_frames": 11,
"box": {"x_min":0, "y_min":58}
}
Design reason: the backend receives enough context for an alert, while the camera frame stays local.
Smart Visual Alarm System | 06
Notes: Explain that detections are not forwarded immediately. The firmware first checks the confidence threshold, then counts positive frames. Once the configured confirmation count is reached and cooldown is not active, it creates a JSON event. The event includes the device ID, event ID, timestamp, label, confidence, confirmation frames, and box coordinates. This is why the Telegram message is informative but still lightweight.

## Slide 7
Python bridge sends Telegram alerts
01
Mosquitto
LAN broker receives smart-visual-alarm/events
02
paho-mqtt
Python subscriber receives the JSON payload
03
validator
Rejects missing fields and invalid confidence
04
sendMessage
requests posts to Telegram Bot API
Backend checks
required fields exist and have correct types
confidence is numeric and between 0 and 1
cooldown prevents repeated Telegram spam
User sees: device, event ID, person label, confidence, confirmation frames, timestamp, and box.
Smart Visual Alarm System | 07
Notes: This is the backend side. The Python bridge is intentionally small because it should be easy to test, audit, and run during a live demo. The script loads environment variables, connects to the MQTT broker, subscribes to the topic, validates the event, formats it into readable lines, and sends it to Telegram. The validation and cooldown are there so malformed messages or repeated events do not create confusing output.

## Slide 8
The bounding box is visible on the device
ESP32-S3-EYE LCD preview with red person bounding box
What this proves
The camera image is processed on the embedded board, and the detection result is rendered immediately as a bounding box on the device display.
Smart Visual Alarm System | 08
Notes: Use this slide as the device-side proof. The important point is that the red bounding box is visible directly on the ESP32-S3-EYE screen. That means the camera frame is captured and processed locally, and the detector result is available before MQTT or Telegram are involved.

## Slide 9
Telegram alert metadata
Telegram alert generated by the Python backend
1
Device
which ESP32-S3-EYE produced the alarm
2
Event
unique event ID for logs and debugging
3
Detection
detected class label, here: person
4
Confidence
model score used to understand alert quality
5
Confirmation frames
how many positive frames supported the alert
6
Timestamp
device uptime when the alert was created
7
Box
bounding-box coordinates from the detector output
The backend forwards readable metadata, not raw camera frames.
Smart Visual Alarm System | 09
Notes: Walk through the rows of the Telegram message. Device identifies the board, Event is a unique alarm ID, Detection is the class label, Confidence is the model score, Confirmation frames shows that this was not a single noisy frame, Timestamp is the device uptime, and Box is the detector bounding box. The main design point is that the user receives enough detail to understand the alert without sending the camera image.

## Slide 10
Possible next steps
Reliability testing
test empty scenes, motion, low light, backlight
record false positives and missed detections
compare thresholds and confirmation-frame settings
Latency metrics
measure camera-to-MQTT timing
measure MQTT-to-Telegram timing
separate model latency from network latency
Deployment hardening
broker authentication or TLS
watchdog and reconnect handling
token rotation and cleaner secret handling
Product features
web dashboard for event history
configurable zones or schedules
optional image snapshot with privacy controls
Smart Visual Alarm System | 10
Notes: This slide shows that the prototype has clear directions for improvement. The most useful next step would be structured testing: different lighting, empty scenes, moving objects, and repeated timing measurements. After that, I would improve security and reliability around MQTT and credentials, and then add product features like event history or configurable detection zones.

## Slide 11
Summary
Implemented capabilities
ESP32-S3-EYE camera, LCD, and detector pipeline
on-device pedestrian model with confidence output
confirmation and cooldown alarm policy
MQTT JSON event publishing
Python Telegram notification bridge
Runtime path
ESP32 camera -> on-device AI -> MQTT event -> Python backend -> Telegram alert
Repository
ernyei13/iot-project-pedestrian-detector
Key idea: useful alarm metadata leaves the device; raw camera frames do not need to.
Smart Visual Alarm System | 11
Notes: Close with the complete system path. The project combines embedded camera capture, on-device pedestrian detection, an alarm policy, MQTT event publishing, and a Python Telegram bridge. The strongest design decision is that the device sends useful event metadata rather than raw camera frames, which keeps the pipeline lightweight and privacy-aware.

## Slide 12
End-to-end system flow
ESP32-S3-EYE local processing: raw frames stay on the board
1
Camera + LCD
Captures RGB565 frames locally and draws the person box on the LCD.
2
On-device AI
Resizes to 224x224x3 and runs ESP-DL PICO_S8_V1 on the board.
3
Alarm decision
Checks confidence, confirmed frames, and cooldown before publishing.
metadata only leaves the device
4
MQTT JSON event
Publishes device, event, label, confidence, count, time, and box.
5
Mosquitto broker
Transports the compact alarm event on the local LAN.
6
Python backend
Validates JSON, formats text, and calls the Telegram API.
7
Telegram alert
Sends a readable alarm message to the user.
Smart Visual Alarm System | 12
Notes: Use this final slide as the complete walkthrough. First, the ESP32-S3-EYE captures the frame and displays the local preview. The AI inference also runs on the board, then the firmware checks the confidence, confirmation-frame count, and cooldown rule. Only after that does compact metadata leave the device. MQTT carries the JSON event to Mosquitto, the Python backend validates and formats it, and Telegram delivers the readable alert to the user.